## Slide 1: Microarchitectural Attacks and Defenses
Yuval Yarom
Ruhr University Bochum

## Slide 2: Outline
About this course
Introduction to x86 assembly
Introduction to the design of modern CPUs

## Slide 3: About This Course

## Slide 4: Staff
Yuval Yarom
Email: yuval.yarom@rub.de
Office: MC 1/40 (temp)
Consulting: by appointment
Robbie Dumitru
Email: robert.dumitru@rub.de
Office: MC 1/48 (temp)
Consulting: by appointment

## Slide 5: Admin
Time table
  Lectures: Tuesday 10am-12pm IC 03/444-414
    Tue 17.10.2023 IC 03/447
    Tue 19.12.2023 IC 03/134
    Possible move to MC later in the semester
  Workshops: Wednesday 12-2pm GB 02/60

## Slide 6: Admin
Time table
  Lectures: Tuesday 10am-12pm IC 03/444-414
    Tue 17.10.2023 IC 03/447
    Tue 19.12.2023 IC 03/134
    Possible move to MC later in the semester
  Workshops: Wednesday 12-2pm GB 02/60
Assessment
  Aiming for 5 practical projects
    Program an attack/defense technique
    Write about it

## Slide 7: Registration
Max 30 students
  Registration via FlexNow
  No mark without registration
  No lab access without registration
Lab access
  Virtual lab, access via SSH
  From your personal IP address (pip)
    See https://noc.rub.de/web/services/pip
  Register today to have a pip address tomorrow

## Slide 8: A Sample Program
baseSqr = base * base
heightSqr = height * height
hypotenuse = sqrt(heightSqr + baseSqr)
asm
Compile
Execute

## Slide 9: First Year Computer Science

## Slide 10: Computer Architecture Course

## Slide 11: Programmers’ Model of Execution
 | Model | Reality
Hardware | Dedicated | Shared
Memory | Uniform | Non-uniform
Execution | Serial | Superscalar
High level languages
Asymptotic rather than concrete performance
Architecture is a minor topic
Focus on abstraction
CPU Vendors’ interests
Eventually, reality kicks in.

## Slide 12: Reality Kicking In

## Slide 13: Learning Outcomes
Diagnose microarchitectural vulnerabilities
Assess software for resilience against microarchitectural vulnerabilities
Design and program proof-of-concept exploits of vulnerable software and hardware
Design and implement countermeasures for software executing on vulnerable hardware

## Slide 14: Introduction to x86 Assembly

## Slide 15: Execution Model
CPU
Fetch
Decode
Execute
RIP
Memory
0x31 0xc0 0x01 0xc6
0
247-1
0x31 0xc0
XOR EAX, EAX

## Slide 16: Instruction Format
INSTR DEST, SRC
XOR EAX, EAX
EAX  EAX EAX

## Slide 17: Registers
R8
R9
R10
R11
R12
R13
R14
R15
General Purpose
RAX
RBX
RCX
RDX
RBP
RSI
RDI
RSP
Special
RIP
RFLAGS
Many more
Floating point
MSR
Control registers
“General purpose” is a bit of a stretch

## Slide 18: GP Registers
Can address part of the register.
  Weird names
  Weirder semantics
Register | Low 32 | Low 16 | Low 8
RAX | EAX | AX | AL
RBX | EBX | BX | BL
RCX | ECX | CX | CL
RDX | EDX | DX | DL
RBP | EBP | BP | 
RSI | ESI | SI | 
RDI | EDI | DI | 
RSP | ESP | SP | 
R8 | R8D | R8W | R8L
R9 | R9D | R9W | R9L
R10 | R10D | R10W | R10L
R11 | R11D | R11W | R11L
R12 | R12D | R12W | R12L
R13 | R13D | R13W | R13L
R14 | R14D | R14W | R14L
R15 | R15D | R15W | R15L

## Slide 19: Instruction Format
INSTR DEST, SRC
XOR EAX, EAX
EAX  EAX EAX

## Slide 20: Instruction Format
INSTR DEST, SRC
XOR EAX, EAX
XOR ESI, ESI
EAX  EAX EAX
ESI  ESI ESI

## Slide 21: Instruction Format
INSTR DEST, SRC
XOR EAX, EAX
XOR ESI, ESI
INC ESI
EAX  EAX EAX
ESI  ESI ESI
ESI  ESI 1

## Slide 22: Instruction Format
INSTR DEST, SRC
XOR EAX, EAX
XOR ESI, ESI
INC ESI
ADD EAX, ESI
EAX  EAX EAX
ESI  ESI ESI
ESI  ESI 1
EAX  EAX ESI

## Slide 23: Instruction Format
INSTR DEST, SRC
XOR EAX, EAX
XOR ESI, ESI
INC ESI
ADD EAX, ESI
CMP ESI, 10
EAX  EAX EAX
ESI  ESI ESI
ESI  ESI 1
EAX  EAX ESI
ESI 10

## Slide 24: Flags
Bits in the RFLAGS register
Store information on last operation (that affects flags)
  CF – Carry
  ZF – Zero
  SF – Sign
  OF – Signed integer overflow

## Slide 25: Instruction Format
INSTR DEST, SRC
XOR EAX, EAX
XOR ESI, ESI
Label:
INC ESI
ADD EAX, ESI
CMP ESI, 10
JNE Label
EAX  EAX EAX
ESI  ESI ESI
ESI  ESI 1
EAX  EAX ESI
ESI 10

## Slide 26: Instructions
MOV – moves between registers or to/from memory
CMOVcc – Conditional move e.g. CMOVNZ moves if the zero flag is not set
PUSH/POP – move to/from [RSP] and change RSP
ADD/SUB/ADC/SBC – Add/subtract without/with carry
CMP – compare
AND/OR/NOT/XOR – Bitwise ops
JMP – unconditional jump
Jcc – conditional jump
CALL/RET – Call subroutine/Return

## Slide 27: Memory
Linear address space
  For our purposes 0 – 247-1
  OS decides which addresses are valid
Addressing components:
  Displacement: 8, 16, or 32 bit constant
  Base: register or 0
  Index: register or 0
  Scale: 1, 2, 4, or 8
address = disp + base + scale*index
LEA – load effective address
Byte order: Little endian
Example: MOV R8W, 1234[8*RAX+RCX]
Moves word at address 8*RAX+RCX+1234 to R8W

## Slide 28: Execution stack
RSP points to the top of the stack
  Grows downward – push decreases RSP
CALL – Pushes RIP to the stack and sets RIP to the new location
RET – Pops RIP from the stack
Calling convention:
  Arguments: RDI, RSI, RDX, RCX, R8, R9
  Return value: RAX
  Scratch: R10, R11
XOR EAX, EAX
XOR ESI, ESI
Label:
INC ESI
ADD EAX, ESI
CMP ESI, EDI
JNE Label
RET

## Slide 29: Inline Assembly
Template: Assembly code
Outputs and inputs: map to program variables
Clobber: locations (registers or memory) that are changed by the code
volatile: indicates that there are side effects
asm [volatile] (template:
outputs: [inputs: [clobber]])
static inline uint64_t rdtscp() {
uint32_t low, high;
asm volatile (
"RDTSCP":
"=a" (low), "=d" (high):
:
"ecx");
return (((uint64_t)high) << 32)
| low;
}
RDTSCP – Read time-stamp counter and processor ID
  EAX – low 32 bits; EDX – high 32 bits; ECX – processor ID

## Slide 30: Intrinsics
C “functions” that provide an API to assembly instructions.
#include <x86intrin.h>
__rdtscp(void *pid)
_mm_clflush(void *addrs)
_mm_lfence()
_mm_mfence()

## Slide 31: Introduction to the Design of Modern CPUs

## Slide 32: Instruction Pipelining
Nominally, the processor executes instructions one after the other
Instruction execution consists of multiple steps
  Each uses a different unit
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back
Instruction Fetch
Instruction Decode
Execute
Memory
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back

## Slide 33: Instruction Pipelining
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back
Instruction Fetch
Instruction Decode
Instruction Fetch
Instruction Decode
Instruction Fetch
Instruction Decode
Instruction Fetch
Instruction Decode
Instruction Fetch
Instruction Decode
Nominally, the processor executes instructions one after the other
Instruction execution consists of multiple steps
  Each uses a different unit
Pipelining increases utilisation by executing steps of multiple instructions
Execute
Memory
Execute
Memory
Execute
Memory
Execute
Memory
Execute
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back
Instruction Fetch
Instruction Decode
Execute
Memory
Write Back

## Slide 34: CPU vs. Memory
Processor
Speed
1 MHz
20×3700 MHz
Memory
Latency
500 ns
50 ns

## Slide 35: Bridging the gap
Cache utilises locality to bridge the gap
Divides memory into lines
Stores recently used lines
In a cache hit, data is retrieved from the cache
In a cache miss, data is retrieved from memory and inserted to the cache
Processor
Memory
Cache
Notes: Another thing that changed since my Apple // days is the processor speed. My apple 2 ran at 1 MHz. My mac runs at 2GHz. Memory speed, however, has not fared so well. The memory on my apple needed half a clock cycle to produce data, whereas modern computers require about 200. When the processor reads from memory it needs to wait. <click> and if it needs to read from the same location again it needs to wait again. <click>. So, we have a speed gap between the processor and the memory.
The cache is the part of the processor that bridges this gap. It is a small memory that is included within the processor. Being small, being closer to the execution core and using more expensive technologies than the main memory mean that the cache is much faster than the memory. On intel the spead ranges from 4 to 50 cycles, depending on the level of cache.
Yada yada

## Slide 36: Set Associative Caches
Memory lines map to cache sets. Multiple lines map to the same set.
Sets consist of ways. A memory line can be stored in any of the ways of the set it maps to.
When a cache miss occurs, one of the lines in the set is evicted.
Memory
Ways
Sets

## Slide 37: A Sample Program
baseSqr = base * base
heightSqr = height * height
hypotenuse = sqrt(heightSqr + baseSqr)

## Slide 38: Nominal program execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:

## Slide 39: Nominal program execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1: 4
r2:
r3:
r4:

## Slide 40: Nominal program execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1: 4
r2: 3
r3:
r4:

## Slide 41: Nominal program execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1: 4
r2: 3
r3: 16
r4:

## Slide 42: Execution dependencies
store r3, hypotenuse
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
mul r1, r2, r3
div r3, 2, r3
store r3, area

## Slide 43: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:

## Slide 44: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:
Start executing first load load

## Slide 45: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:
Start executing second load
Suppose height is in the cache and second load terminates first

## Slide 46: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:
Start executing the multiply instruction

## Slide 47: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:
When the first load completes

## Slide 48: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1: 4
r2: 3
r3:
r4:
retire all completed instructions

## Slide 49: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1: 4
r2: 3
r3:
r4:
… and proceed

## Slide 50: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1: 4
r2: 3
r3:
r4:
Proceed
… and also here
Why not retire out-of-order?

## Slide 51: Why not retire early
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2: 3
r3:
r4:
Early retire stores a result in the architectural state

## Slide 52: Why not retire early
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2: 3
r3:
r4:
A later fault leaves the processor in an inconsistent state!
Early retire stores a result in the architectural state

## Slide 53: How does it all work?
53
Frontend
Loads speculated instruction stream
Decodes to micro-ops
Dispatches to Execution Engine
Reorder instructions for retirement
Execution Engine
Tracks dependencies between micro-ops
Executes ready micro-ops
Updates frontend on progress
Memory Subsystem
Manages caches, memory order and coherency
Frontend
Loads speculated instruction stream
Decodes to micro-ops
Dispatches to Execution Engine
Reorder instructions for retirement
Execution Engine
Tracks dependencies between micro-ops
Executes ready micro-ops
Updates frontend on progress
Memory Subsystem
Manages caches, memory order and coherency

## Slide 54: The frontend

## Slide 55: The execution engine

## Slide 56: The memory subsystem

## Slide 57: Summary
X86-64 assembly – you need to know
Modern computers are complex
Next workshop: practise assembly
Next lecture: Flush+Reload
  Reading: Yarom and Falkner, “Flush+Reload: a High Resolution, Low Noise, L3 Cache Side-Channel Attack,” USENIX Security 2014