## Slide 1: Software Guard eXtensions (SGX)

## Slide 2: Operating Systems
Controls sharing of system resources
Enforces protection

## Slide 3: Operating Systems
Controls sharing of system resources
Enforces protection
Can be compromised
Not always trustworthy

## Slide 4: Operating Systems
Controls sharing of system resources
Enforces protection
Can be compromised
Not always trustworthy
And has superpowers

## Slide 5
SGX

## Slide 6: SGX (Software Guard eXtensions)
CPU hardware feature designed to allow (remote) secure computation
“Developers can partition their application into processor-hardened enclaves or protected areas of execution in memory that increase security even on compromised platforms. ”
“Confidentiality and integrity: Enforced at the operating system, BIOS, VMM, SMM, or TEE layers even in the presence of privileged malware.”
“Remote attest and provision: A remote party can verify an application enclave identity and securely provision keys and other sensitive data to the enclave”
Present on all Intel CPUs since 2016 (SkyLake)

## Slide 7: SGX Security Model
User Space
OS Kernel
VMM
SMM
RAM
HW
User Space
OS Kernel
VMM
SMM
CPU

## Slide 8: SGX Security Model
User Space
OS Kernel
VMM
SMM
RAM
HW
CPU
Enclave
Attestation
Remote
Client

## Slide 9: SGX Memory Management
Enclave pages are encrypted and authenticated
OS allocates pages
Hardware verifies mapping
Abort page semantics
Secure page swap
Memory
SGX Memory
Enclave Page Cache (EPC)
Merkle Tree
Admin
Page Table
EPCM
Enclave ID

## Slide 10: SGX Security Model: The Fine Print
“Intel SGX does not provide explicit protection from side-channel attacks, it is the developer's responsibility to address side-channel attack concerns.”
You can’t break our side channel protections, if we don’t have any
Intel SGX Developer Guide, Page 39/40

## Slide 11: Controlled Channels Attacks (Xu et al. IEEE SP 2015)
OS controls page table – marks all as invalid
Gets access on enclave interrupt
Trace page accesses
PT
EPCM
Enc. ID

## Slide 12: OS Control
Interrupts are not required (Van Bulck et al. USENIX Sec. 2017)
  Monitor accessed and dirty bits on page tables
  Cache attacks on PTEs
Isolate core
Fixed CPU frequency
Monitor performance counters
Timer interrupts

## Slide 13: SGX Step (Van Bulck et al. SysTEX 2017)
Library for controlling SGX execution
Exposes page maps to user space
Exposes APIC interrupts to user space
Allows user control at enclave interrupts
High resolution, low noise microarchitectural attacks

## Slide 14: Meltdown-type attacks

## Slide 15: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:

## Slide 16: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:
Start executing first load load

## Slide 17: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:
Start executing second load
Suppose height is in the cache and second load terminates first

## Slide 18: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:
Start executing the multiply instruction

## Slide 19: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:
When the first load completes

## Slide 20: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1: 4
r2: 3
r3:
r4:
retire all completed instructions

## Slide 21: Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1: 4
r2: 3
r3:
r4:
… and proceed
Why not retire out-of-order?

## Slide 22: Why not retire early
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2: 3
r3:
r4:
Early retire stores a result in the architectural state

## Slide 23: Why not retire early
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2: 3
r3:
r4:
A later fault leaves the processor in an inconsistent state!
Early retire stores a result in the architectural state

## Slide 24: Traps in Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r1
div r1, 2, r1
store r1, area
CPU
r1:
r2:
r3:
r4:
Start executing second load
Suppose height is an invalid address

## Slide 25: Traps in Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:
Mark as an error, but continue executing until all older instructions retire

## Slide 26: Traps in Out of Order Execution
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1: 4
r2:
r3:
r4:
Mark as an error, but continue executing until all older instructions retire
Raise Trap

## Slide 27: Traps in Out of Order Execution
But while we’re waiting…
Dependent instructions
Start executing
Mark as an error, but continue executing until all older instructions retire
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:

## Slide 28: Traps in Out of Order Execution
Mark as an error, but continue executing until all older instructions retire
But while we’re waiting…
Dependent instructions
Start executing
load base, r1
load height, r2
mul r1, r1, r3
mul r2, r2, r4
add r3, r4, r3
sqrt r3, r3
store r3, hypotenuse
mul r1, r2, r3
div r3, 2, r3
store r3, area
CPU
r1:
r2:
r3:
r4:

## Slide 29: Load instructions
Execution Engine
Virtual Address

## Slide 30: Load instructions
Memory Pipeline
L1 Cache
L2 Cache
Execution Engine
Virtual Address
Physical Address
Data

## Slide 31: Load instructions
Memory Pipeline
L1 Cache
L2 Cache
Execution Engine
Virtual Address
Physical Address
Data

## Slide 32: Using a Covert Channel
i = *pointer;
y = array[i * 4096];
Cache
3
3
array
pointer
The number of the day

## Slide 33: Using a Covert Channel
It is 3!
array
pointer
i = *pointer;
y = array[i * 4096];
Cache
3
3

## Slide 34: Meltdown

## Slide 35: Meltdown
i = *pointer;
y = array[i * 4096];
Cache
3
array
Kernel space (protected)
pointer

## Slide 36: Meltdown
array
Kernel space (protected)
pointer
i = *pointer;
y = array[i * 4096];
Cache
3
It is 3!

## Slide 37: Handling Faults
A fault kills the process. How do we recover the channel?
Spawn a new process
Use a signal handler
?

## Slide 38: Fault suppression
if (train) {
a = *ptr
b = array[a * 4096]
}
if (_xbegin() == _XBEGIN_STARTED) {
a = *ptr
b = array[a * 4096]
_xend()
}

## Slide 39: Meltdown Countermeasure - KPTI
Use a separate address space for the kernel
  Overhead when crossing address space
Newer processors transiently return 0
Kernel space (protected)
Process
Kernel
Mapping of process

## Slide 40: Foreshadow

## Slide 41: Meltdown on Enclaves
i = *pointer;
y = i * 4096;
z = array2[y];
L1 Cache
pointer
array2
EPC
Enclave data
(=3)
Attackers data
I’m still alive?!
virtual memory
array2[4096]
array2[8192]
array2[12288]
3
-1
Abort Page Semantics
no leakage
…
AES

## Slide 42: Foreshadow
i = *pointer;
y = i * 4096;
z = array2[y];
L1 Cache
pointer
array2
EPC
Enclave data (=3)
Aha! data=3
virtual memory
3
3
array2[4096]
array2[8192]
array2[12288]
3
Attackers data
Address translation failed
Instruction flagged to fault at retirement
No need to apply permission checks (abort page semantics) as instruction will fault later anyway
mprotect(…)
AES
L1 hit

## Slide 43: Foreshadow-OS (Weisse et al. 2018)
Disk
Stale reference remains after page out
  Data cached in L1 can leak
Countermeasure: Invert bits in page entry
Page Table
Memory

## Slide 44: Philosophy 101
If a tree falls and no one is around to hear it, does it make a sound?
Should we care?
Well, it depends…
SGX

## Slide 45: Security 101
If a machine was hacked,
no one knows,
and there is no data on it…
Should we care?
SGX Machine

## Slide 46
Foreshadow
Can steal ~100% of the data ~100% of the time
Can also steal attestation EPID private keys

## Slide 47: Remote Attestation: Establishing Trust Remotely
I am software running inside an SGX enclave. Key share:
quote
Verify Quote with Intel
3. I believe you. Key share:
4. Session key:
Intel Attestation Service
(IAS)
Client
EPID key
quote
Takeaway: trust is based on the EPID key

## Slide 48: With a Enhanced Privacy comes Enhanced responsibility
EPID epic feature: privacy guarantees
Million signatures are unlinkable
No one knows who signed what
Enhanced Privacy ID
A single extracted EPID key can be used to sign millions of unlinkable signatures
One compromised key erodes trust in the entire ecosystem

## Slide 49: AaaS (Attestation as a Service)
@ForeshadowAaaS Will attest to anything tweeted at it
Reduced cost of hackership – no need to buy an SGX machine
Hacker’s privacy guaranteed by EPID protocol
Attestation server returns Group_Out_Of_Date
At disclosure, SGX Keys were still not revoked (despite weeks of advances notice)
Blocked by Twitter

## Slide 50: Foreshadow Mitigations
Flush L1 Cache after enclave exits and “page-in/out” operations
  New L1 flush “instruction” added
Disable HyperThreading
Have two sets of Attestation/Sealing keys
  For HyperThreading On/Off
Patch your machine!
L1 Cache
Core 1
Core 2

## Slide 51: Foreshadow-VMM (Weisse et al. 2018)
Virtual Machine
Invalid guest mappings transiently use the guest physical address
Countermeasure
  Flush L1-D on VM exits
  Disable hyperthreading or use gang scheduling
Page Table
EPT
Memory

## Slide 52: Microarchitectural Data Sampling

## Slide 53: What if the data is not in the cache?
Memory Pipeline
L1 Cache
L2 Cache
Execution Engine
Line Fill Buffers
Physical Address
Physical Address
Data
Data
Data

## Slide 54: Microarchitectural Data Sampling (MDS)
Data leaks not only from the cache
There are multiple buffers that can leak information
  Line fill buffers – used when filling the cache
  Store buffers – reorder load and store instructions
  Load Ports – some other cases
Bonus: traps are not necessary
  Microcode assists
  TSX abort
Execution Engine
Store Buffers
Memory Pipeline
Line Fill Buffers
L1 Cache
L2 Cache
Countermeasure:
  Prevent access to sensitive data
  Flush buffers containing sensitive data
  Zero sensitive data

## Slide 55: CacheOut and CrossTalk
We can move data to buffers after they are flushed
CacheOut:
  L1 eviction go to the line fill buffers
  Revives Foreshadow
CrossTalk:
  Can read from a staging buffer via the line fill buffers
  Can steel randomness from SGX enclave
Execution Engine
Store Buffers
Memory Pipeline
Line Fill Buffers
L1 Cache
L2 Cache
Last Level Cache
Staging Buffer
CrossTalk

## Slide 56: Summary
SGX
  Strong security guarantees against OS attackers.
  Enables strong side channel attacks
Causes of Meltdown-type attacks
Handling faults
Where information comes from
Some defences
Reading for next week:
  Tian et al., SoK: “Plug & Pray” Today – Understanding USB Insecurity in Versions 1 through C, IEEE SP 2018