## Slide 1: Flush-Based Attacks

## Slide 2: Today
Flush+Reload
Recovering missing bits from RSA keys
Performance degradation attacks
Flush+Flush

## Slide 3: Bridging the gap
Cache utilises locality to bridge the gap
Divides memory into lines
Stores recently used lines
In a cache hit, data is retrieved from the cache
In a cache miss, data is retrieved from memory and inserted to the cache
Processor
Memory
Cache
Notes: Another thing that changed since my Apple // days is the processor speed. My apple 2 ran at 1 MHz. My mac runs at 2GHz. Memory speed, however, has not fared so well. The memory on my apple needed half a clock cycle to produce data, whereas modern computers require about 200. When the processor reads from memory it needs to wait. <click> and if it needs to read from the same location again it needs to wait again. <click>. So, we have a speed gap between the processor and the memory.
The cache is the part of the processor that bridges this gap. It is a small memory that is included within the processor. Being small, being closer to the execution core and using more expensive technologies than the main memory mean that the cache is much faster than the memory. On intel the spead ranges from 4 to 50 cycles, depending on the level of cache.
Yada yada

## Slide 4: Cache Consistency
Memory and cache can be in inconsistent states
  Rare, but possible
Solution: Flushing the cache contents
  Ensures that the next load is served from the memory
Processor
Memory
Cache

## Slide 5: The Flush+Reload Attack
Flush a memory line from the cache
Wait a bit
Measure time to load line
  slow-> no access
  fast-> access
Repeat
Processor
Memory
Cache
Notes: Reminder: Fast 50 cycles. Slow 200. Measurement adds about 30 cycles.
Wrap-up – the weakness is that the spy can monitor access to shared memory lines and consequently infer information about the data the victim processes

## Slide 6: Flush+Reload
Time
flush
wait wait wait wait
Reload
flush
wait wait wait wait
Reload
flush
wait wait wait

## Slide 7: Flush+Reload
Time
flush
wait wait wait wait
Reload
flush
wait wait wait wait
flush
wait wait wait
Spy
Victim
working working
working working
access

## Slide 8: Detour - Virtual Memory
Processes execute within a virtual address space
  Virtual pages map to physical frames

## Slide 9: Sharing
Frames can be shared by multiple processes
  Read only sharing maintains functional isolation
  Protection using Copy-on-write

## Slide 10: Causes of sharing
Content-aware sharing
  Pages from the same file have identical content
  Shared program or library code
    Can also share constant data
  Shared images in PaaS clouds
Content-based sharing (a.k.a. page deduplication)
  The system identifies and coalesces identical pages
  Implemented in many hypervisors and in most modern operating systems

## Slide 11: Demo

## Slide 12: The RSA Encryption System
The RSA encryption is a public key cryptographic scheme
C = Me mod N
M
C
M = Cd mod N
Key Generation:
Select random primes p and q
Calculate N = pq
Select a public exponent e(=65537)
Compute d=e-1 mod φ(N)
(N, e) is the public key
(p, q, d) is the private key

## Slide 13: Square and Multiply Exponentiation
Operation | x | i | di
 | 1 | 2 | 101
Square | 1 | 2 | 101
reduce | 1 | 2 | 101
Multiply | 11 | 2 | 101
reduce | 11 | 2 | 101
Square | 121 | 1 | 101
reduce | 21 | 1 | 101
Square | 441 | 0 | 101
reduce | 41 | 0 | 101
Multiply | 451 | 0 | 101
reduce | 51 | 0 | 101
Example:
115 mod 100 =
161,051 mod 100 = 51
x ⟵1
for i ⟵|d|-1 downto 0 do
x ⟵x2 mod n
if (di = 1) then
x = xC mod n
endif
done
return x
The private key is encoded in the sequence of operations !!!
Notes: Old implementation – not in use

## Slide 14: Demo

## Slide 15: Flush+Reload on Square-and-Multiply

## Slide 16: Why not AMD?
Multilevel cache hierarchy
Inclusive LLC: stores copies of all data in higher level caches
Exclusive LLC: does not store data cached in higher level caches
Non-inclusive LLC: not strictly inclusive. (Can be exclusive.)
Core 0
L1-I
L1-D
L2
Core 1
L1-I
L1-D
L2
LLC

## Slide 17: Defences

## Slide 18: Performance Degradation
Allan et al. “Amplifying Side Channel Through Performance Degradation” ACSAC 2016
See also: Cabrera Aldaya and Brumley. “HyperDegrade: From GHz to MHz Effective CPU Frequencies”, USENIX Security 2022

## Slide 19: Flush+Reload
Time
flush
wait wait wait wait
Reload
flush
wait wait wait wait
flush
wait wait wait
Spy
Victim
working working
working working
access

## Slide 20: Timing matters
Time
flush
wait wait wait wait
Reload
flush
wait wait wait wait
flush
wait wait wait
Spy
Victim
working working
working working
access
Reload
Access missed due to temporal overlap

## Slide 21: Probability of a probe miss
Ratio of probe time to slot length

## Slide 22: Probing OpenSSL ECDSA
For secp256k1, operation times are:
  Addition: 2,892 cycles
  Doubling: 3,086 cycles
  Everything else: negligible
To avoid aliasing errors, need to probe at least once every 1,450 cycles
Limitations on probing
  Each probe takes 450 cycles.
  At the required probe rate, we can expect a 37% miss rate

## Slide 23: Solution: slow the victim down
Flushing data or code forces the victim to retrieve it from the memory
Performance degradation attack:
  Find frequently used code lines
    For example, usingprofiling information
  Repeatedly flush them from the cache
Processor
Memory
Cache
Notes: Reminder: Fast 20ns. Slow 80ns including a 10ns measurement overhead
Note that the attack works across cores.

## Slide 24: SPEC Results

## Slide 25: Attacking OpenSSL
Use two threads to flush three addresses spanning the inner loop in the bignum multiplication code
  Add slowed by a factor of 53 (153,709 cycles)
  Double slowed by a factor of 41 (126,282 cycles)
Monitor four memory locations: one in add, one in double and two in the call chain of invert
Probe each monitored location once every 17,000 cycles

## Slide 26: Flush+Flush
Gruss et al. “Flush+Flush: A Fast and Stealthy Cache Attack”, DIMVA 2016

## Slide 27: Flush+Flush
Flush time depends on cache residency
Small differences, variable baseline

## Slide 28: Improvements
Timing depends on core and slice. Can improve accuracy through calibration
  Didier and Maurice, “Calibration Done Right: Noiseless Flush+Flush Attacks.”, DIMVA 2021
Avoiding fences increases difference between hit and miss
  Ding et al., “A Cross-Platform Cache Timing Attack Framework via Deep Learning”, DATE 2022

## Slide 29: Summary
Flush+Reload and related attacks
Amplification through performance degradation
Next: Prime+Probe Attacks
  Read: Osvik, Shamir, and Tromer, “Cache attacks and Countermeasures: The Case of AES”, CT-RSA 2006