## Slide 1: Prime+Probe

## Slide 2: Cache Attacks
Program
History
Cache
State
Execution
Time

## Slide 3: Cache Attacks
Program
History
Cache
State
Execution
Time

## Slide 4: Bridging the gap
Cache utilises locality to bridge the gap
Divides memory into lines
Stores recently used lines
In a cache hit, data is retrieved from the cache
In a cache miss, data is retrieved from memory and inserted to the cache
Processor
Memory
Cache
Notes: Another thing that changed since my Apple // days is the processor speed. My apple 2 ran at 1 MHz. My mac runs at 2GHz. Memory speed, however, has not fared so well. The memory on my apple needed half a clock cycle to produce data, whereas modern computers require about 200. When the processor reads from memory it needs to wait. <click> and if it needs to read from the same location again it needs to wait again. <click>. So, we have a speed gap between the processor and the memory.
The cache is the part of the processor that bridges this gap. It is a small memory that is included within the processor. Being small, being closer to the execution core and using more expensive technologies than the main memory mean that the cache is much faster than the memory. On intel the spead ranges from 4 to 50 cycles, depending on the level of cache.
Yada yada

## Slide 5: Set Associative Caches
Memory lines map to cache sets. Multiple lines map to the same set.
Sets consist of ways. A memory line can be stored in any of the ways of the set it maps to.
When a cache miss occurs, one of the lines in the set is evicted.
Memory
Ways
Sets

## Slide 6: The Prime+Probe Attack [OST06]
Allocate a cache-sized memory buffer
Prime: fills the cache with the contents of the buffer
Probe: measure the time to access each cache set
  Slow access indicates victim access to the set
The probe phase primes the cache for the next round
Memory

## Slide 7: Demo

## Slide 8: Sample Victim: Data Rattle

## Slide 9: Cache Fingerprint of the Rattle Program

## Slide 10: Finding Eviction Sets
Address
0 | 1 | 2 |  | 63
64B | 64B | 64B | · · · | 64B
64B | 64B | 64B | · · · | 64B
· · · | · · · | · · · | · · · · · · · · · | · · ·
64B | 64B | 64B | · · · | 64B
Offset
Set
Tag
0
5
6
11
12

## Slide 11: Out-of-Order Execution
RTDSCP
MOV ESI, RAX
LFENCE
MOV RBX, [RDI]
MOV RBX, [RDI + 4096]
…
MOV RBX, [RDI + 28672]
RDTSCP
SUB EAX, ESI
RDTSC
(hit)
RDTSC
(miss)
Out-of-Order Execution can mask cache misses

## Slide 12: Controlling Execution Order
RDTSC
(hit)
RDTSC
(miss)

## Slide 13: Creating Dependencies
RTDSCP
MOV ESI, RAX
MOV RDI, [RDI]
MOV RDI, [RDI]
…
MOV RDI, [RDI]
RDTSCP
SUB EAX, ESI
XOR ECX, ECX
RTDSCP
MOV ESI, RAX
ADD ECX, [RDI + ECX]
ADD ECX, [RDI + ECX + 4096]
…
ADD ECX, [RDI + ECX + 28672]
RDTSCP
SUB EAX, ESI
Percival (2005)
Set memory to zero
Use arithmetic to force dependencies
Osvik, Shamir, Tromer (2006)
Follow a linked list
Also known as Pointer chasing

## Slide 14: Fighting the Prefetcher
Prefetchers try to pre-emptively load data into caches to serve identified access patterns.
A common pattern is accessing memory at fixed steps.
  Scanning an array.
Prefetching in Prime+Probe may kill the attack
Solution: Randomize probe order
A
A+s
A+2s
A+3s
A+4s
75
79
77
81
0 | 1 | 2 |  | 63

## Slide 15: Attacking AES
Plaintext
Ciphertext
AddRoundKey
SubBytes
ShiftRows
MixColums
AddRoundKey
SubBytes
ShiftRows
AddRoundKey
x9
Lookup table

## Slide 16: Attacking AES

## Slide 17: AES T-table access
Assume we know the plaintext and the index (s0>>24)
  We can recover the most significant byte of the key
s0 = plaintext ^ key
t0 = Te0[s0>>24]

## Slide 18: Spatial Resolution
Prime+Probe detects access to cache sets
Can only get the four MSBs of the index
Aliasing is not a problem
  For this attack!
Cache Line 0
Cache Line 1
Cache Line 2
Cache Line 3
Cache Line 4
Cache Line 5
s0 = plaintext ^ key
t0 = Te0[s0>>24]

## Slide 19: Temporal Resolution
Probing 64 cache sets takes a minimum of cycles
AES encryption takes about 112 cycles
How do we measure only the first access?
Measure this
With this

## Slide 20: Synchronous Attack
Attack: Prime, AES, Probe
A table has 256 entries of 4 bytes each  16 cache lines
Probability of no access to a cache set: (15/16)40 or approx. 7.6%
On average ~5 cache lines not accessed during encryption
Eliminate impossible keys
Plaintext
Ciphertext
AddRoundKey
SubBytes
ShiftRows
MixColums
AddRoundKey
SubBytes
ShiftRows
AddRoundKey
x9
Lookup table
s0 = plaintext ^ key
t0 = Te0[s0>>24]

## Slide 21: Handling Noise
General strategy
  Average
OS Activity
  Remove outliers
Spy activity
  Normalize

## Slide 22: PP Attack on AES - Results

## Slide 23: PP Attack on AES – More Results

## Slide 24: Another look at the data
Given plaintext and a guess of a key byte, we can predict the probability that a cache line is accessed:
  Cache line of p^key: 100%
  Other lines in same table: 1-(15/16)39 = 91.9%
Probe time correlates with cache misses

## Slide 25: Correlation Attack
Pick a cache set in the table
For a sequence of plaintext do PP on the cache set (filter outliers)
For each key guess, determine probability of access to cache set
Compute the Pearson correlation between each key and measurements
  Pearson correlation

## Slide 26: Final round attack
Given ciphertext and (last round) key guess, determine cache access
Correlation attack breaks the full key
Plaintext
Ciphertext
AddRoundKey
SubBytes
ShiftRows
MixColums
AddRoundKey
SubBytes
ShiftRows
AddRoundKey
x9
Table Lookup

## Slide 27: L1-Instruction Cache
So far we targeted the L1 Data cache.
But there are other caches. Can we target them?
L1-I – caches program code.
  Why do we need a separate cache?
Need to have code in specific memory location.
Core 0
L1-I
L1-D
L2
Core 1
L1-I
L1-D
L2
LLC
JMP .+4096
JMP .+4096
RET

## Slide 28: AssemblyLine
A library for generating assembly code
In active development – ask if interested

## Slide 29: Summary
Prime+Probe
  Attack theory
  … and practice
Attacking AES
  Ideal scenario
  Basic noise handling
  Correlation attacks
Next lecture
  Recovering partial RSA keys
  Read: Heninger and Shacham, “Recovering RSA Private Keys from Random Key Bits”, CRYPTO 2009